INTRODUCTION
In recent years, proactive communication between vehicles became a more prevalent matter of research. Today many manufacturers try to implement new technology into their vehicles, aiming at improved security and comfort for the passengers. The needed communication infrastructure is developing fast, with several technologies available to choose from depending on the use case.

One important use case of this new technology is the cooperative maneuver coordination, as this cooperation between vehicles enables an even higher degree of automation, leading to more efficient traffic and safety in complex driving situations.

Independently from the deployment, as a centralized or decentralized approach, this high level of cooperation has strict performance requirements of the communication links. Yet there is no guarantee if these requirements will be satisfied at all times due to poor network coverage or propagation conditions.

As a priori knowledge of the communication quality may serve to adjust and enhance the level of cooperation, this study performs a research in currently available communication prediction methods and evaluates these approaches in terms of their applicability to the use case of autonomous cooperative maneuver coordination.

The paper is structured as follows: First, it will give an overview of related works. Following that, Sect. 3 will introduce the concept of cooperative maneuver cooperation and analyze its requirements on communication. In Sect. 4 current research of prediction methods is being explored. The following discussion will evaluate the existing methods in terms of their applicability on cooperative maneuver coordination and lay the foundation for the conclusion.

Section 4 which reviews have been conducted in the same area of research. Following that, the methods are being depicted, structured in the methods they used for their predictions. Section 3 compares the methods and the respective works, giving an overview I a brief comparison table. Lastly the conclusion identifies areas yet to be further researched and tries to give an overview of the upcoming works.

As these functions rely on communication, reliable links are crucial for their operation and functionality. Given the fact, that a perfect network coverage at any time and any location is out of reach, it is beneficial to predict the quality of the network in order to adapt applications to the current and future situation, but yet no standard has emerged and network quality prediction is still an area of research.

This study gives an overview of considerable methods for the prediction of the network quality in terms of different indicators and for different use cases.

The paper is structured as follows: First, it will give an overview of related works, which reviews have been conducted in the same area of research. Following that, the methods are being depicted, structured in the methods they used for their predictions. Section 3 compares the methods and the respective works, giving an overview I a brief comparison table. Lastly the conclusion identifies areas yet to be further researched and tries to give an overview of the upcoming works.

RELATED WORKS
As this work tries to give a comprehensive overview of prediction methods with a given set of constraints, other works providing overviews of methods or constraits must not be neglected. These can be grouped into different categories based on the research topics they portray.

Network Basics
Existing studies give a great overview of the challenges faced in vehicular communication. While Mecklenbräuer et al, 2011 gives an overview the available technologies, its focus lies in the depiction of the communication channels, the various scenarios (V2V, V2I, cellular), the metrics (e.g. fading, path loss and doppler shift) as well as the models (e.g. raytracing or stochastic models) for their simulation.

For the estimation of the communication channel, traditionally pilot symbols are being used, which contain no data, but by which the receiver is able to estimate and equalize received data. This estimation is the key element in achieving low bit error rates (BER) but not trivial.

Existing pilot patterns such as the one from 802.11p were not designed for highly mobile networks, thus leading to decreased performance in these scenarios. Some of our the reviewed methods try to take the prediction as an advantage for channel estimation, as such it is crucial to understand and distinct these terms.

Communication Prediction
As by now, efforts in the standardization of vehicular communication prediction are undertaken, the 5GAA summarized the key concept of QoS prediction and its use cases and challenges. Notably, the whitepaper identifies possible deployment methods, namely Over-The-Top and Mobile Network Operator prediction, as well as

\section{Cooperative Maneuver Coordination}
Cooperative Maneuver Coordination is the aim of making automated vehicles influence the each others behaviour and enabling joint driving maneuvers, making road traffic safer and more efficient.
The concept consists of multiple use cases, among others \cite{bobanConnectedRoadsFuture2018}:
\begin{itemize}
\item lane changing
\item platooning
\item cacc (cooperative adaptive cruise control)
\item intersection control
\item collision avoidance
\end{itemize}
Hereby different approaches exist, either as centralized \cite{mengluICTInfrastructureCooperative2018} or decentralized cooperation \cite{llatserCooperativeAutomatedDriving2019,fortelleNetworkAutomatedVehicles2014}.

In a centralized cooperation, a central entity such as a RSU, gains global knowledge by the usage of its own sensor data and direct communication with the vehicles in its coordination range and thereby plans optimal maneuvers in terms of efficiency and safety.

The decentralized approach does not rely on a central entity, but rather leaves the planning to the vehicles, which adapt their maneuvers based on maneuver intentions shared by surrounding vehicles in order to achieve locally optimal traffic patterns.

Without going too much into the details of implementation methods for the coordination, we rather want to take a look at the aspect of communication. Several works investigated the requirements for the communication links. Typical KPIs (Key Performance Indicators) are end-to-end latency, reliability, data rate (per vehicle) and the communication range.

Boban et al. \cite{bobanConnectedRoadsFuture2018} suggest a latency of sub 3 to 100 ms, a required data rate of 1.3 to 25 MB/s, depending on the degree of sensor data dissemination, and a transmission reliability of over 99\%.

As stated in \cite{llatserCooperativeAutomatedDriving2019}, the number of exchange messages and their contained amount of data need to adapt dynamically in order to prevent channel congestion, as it is apparent that the aforementioned link requirements cannot be met at all times. Furthermore vehicles need to interact with their environment even without these cooperation messages.

The aim of this work is to evaluate existing communication prediction methods in terms of their applicability on the cooperative maneuver coordination. Therefore we first need to identify possible prediction scenarios and use cases.

If we take the use case of intersection control and collision avoidance for example, it is clear, that vehicles are approaching each other from different directions and the requirements on the reliability on the communication between these vehicles are of a higher priority than the communication with other vehicles of the area. While a global prediction is attractive, the close-to-mid range prediction is far more relevant in such use cases.

The most interesting parameters are the reliability, e.g. measured in packet loss, and latency, as they decide whether the communication is stable enough in order to be used for cooperation. Otherwise the predictions can be used to initiate safety measures such as increased distancing against the desire for perfect efficiency.

METHODS
Methods for Communication Prediction can be primarily split into two categories, on the one hand the channel quality prediction for the immediate future and on the other hand channel quality or related indicator prediction for the short- to long-term future.

\subsection{Immediate Channel Prediction Schemes}
The immediate channel quality prediction is mainly targeted as an extension resp. an alternative for traditional channel quality estimation using pilot symbols.
Over the years, a large number of works using different prediction algorithms emerged.

Traditional prediction schemes based on channel propagation models or past channel information can be classified into the three methods: Sum-of-Sinusoids (SOS) Model, Basis Expansion (BE) Model and Autoregression (AR) Model.

Common to these traditional methods is their time frame, predicting only several milliseconds into the future for high velocity nodes. This time frame is small, but enables adaptive transmission techniques such as adaptive modulation, channel coding or power control and even adjustments in high level applications in contrast to using estimated CSI, which is instantaneously outdated at higher velocities.

\subsubsection{AR}
The AR model uses previous channel samples in form of CSI in combination with time-variant coefficients. These channel coefficients need to be computed using estimation techniques, either static, such as Wiener filter or LS criterion, or adaptive, such as various LMS or RLS filters.

One of the most acclaimed works in this area of research was conducted by Duel-Hallen et al. \cite{duel-hallenLongrangePredictionFading2000}. Their research was performed in order to provide a long-range channel prediction algorithm by predicting the channel coefficients up to hundreds of symbols ahead using LMS filtering, which is adaptive and computationally less expensive than RLS filtering.
The method was tested against simulated and measured data of static and mobile environments and yielded improved BER when combined with adaptive channel modulation.

\subsubsection{SOS}
In contrast to AR, the SOS model approximates the physical propagation process by modelling the channel as a linear combination of complex sinusoids. This model provides a good predictive performance, but only in cases where the channel parameters consisting of amplitude and Doppler frequency are static.

Noteworthy are the MUSIC and ESPRIT algorithms used in \cite{wongWLC435LowComplexityAdaptive2006,wongJointChannelEstimation2005,semmelrodtInvestigationDifferentFading2003,tealSimulationPerformanceBounds2001,vaughanShorttermMobileChannel2000,chenNewApproachesChannel2006} where \cite{wongWLC435LowComplexityAdaptive2006} provides a reduced complexity ESPRIT algorithm, that tries to reduce the computational complexity of time-variant parameters seen in realistic channels.

\subsubsection{BE}
The BE model describes the channel as a linear set of basis functions, such as complex exponential (CE) or discrete prolate spheroidal (DPS) sequences, multiplied by coefficients, which are obtained through analysis of the pilot data. Zemen et al. \cite{zemenMinimumEnergyBandLimitedPredictor2007} provide a method based on time-concentrated and band-limited DPS sequences. The predictor dynamically selects the spanned subspace with the smallest reconstruction error and utilizes it in order to predict the channel.

While the DPS-BEM outperforms DPS-CEM in numerical simulations, yet no comparison is concluded against SOS and AR models. Of the latter two, AR models seem to perform better in terms of their prediction horizon and computational complexity as stated in \cite{semmelrodtInvestigationDifferentFading2003}.

\subsubsection{Machine Learning}

II. Short- to Long-Term Prediction Schemes
The short- to long-term prediction is targeted rather at high-level applications that need long term knowledge for adjusted communication. Therefore predictions are mostly performed for indicators such as throughput, latency or package loss, which are linked to the channel quality.

I. Immediate Channel Prediction Schemes
Tradional History Based Models:
Traditional history based prediction schemes can be classified into the three methods: Sum-of-Sinusoids (SOS) Model, Basis Expansion (BE) Model and Autoregression (AR) Model.
Common to these traditional methods is their time frame, predicting only several milliseconds into the future for high velocity nodes. This time frame is small, but enables adaptive transmission techniques such as adaptive modulation, channel coding or power control and even adjustments in high level applications in contrast to using estimated CSI, which is instantaneously outdated at higher velocities.
The aforementioned AR model uses the outdated CSI in order to predict the future CSI, meaning that no knowledge of physical parameters is needed.

I. Connectivity Map Based Methods
We start off the examination of works with so-called connectivity maps as they present the most simple concept for prediction of future connectivity. Mobile nodes such as vehicles share their experienced network quality with a central back end using their data channels, which in turns aggregates all the received data in a map.

This concept differs from the related network coverage maps, which use mathematical models in order to determine network coverage and quality at a given location.

The following methods mainly distinguish in the data that is aggregated and thereby predicted as well as the data processing that is performed for determining the future network quality at a given location.

Kelch et al. [] examine this concept in the vehicular application, focusing on the acquisition and matching of data, which includes CQI values queried for generated TCP/IP traffic on their cellular modem, as well as the coordinated gathered by a GPS module. In order to make good predictions for map segments, they examine a map segmentation method called Jump-P [], which outperforms simple fixed length segmentation in terms of the trade-off between the number of needed map segments and the RMSE of the pooled data. The CQI values shared to the sender determine the block size, as better channel conditions allow for a more optimized data transmission, thus enabling an estimation of the theoretical throughput for a given CQI value.

Summarizing, this method enables a prediction of the theoretical throughput by previously collected CQI values. Only a small range of CQI values lead to tolerably accurate predictions, as values below 20 rarely appeared and values above 25 were exceedingly inaccurate.

A similar approach is performed by Pögel et al. [], but in contrast they are collecting different data in the form of RSSI (which is part of CQI) as well as used cells, actual bandwidth and latency at a given location. This leads to a more accurate prediction, but as the authors show, the accuracy is highly dependant on external factors such as average speeds, congestion and weather as they show in their tests performed on different weekdays. As the map simply delivers collected data, it is not self-adjusting to these external factors.

The only comparable measurement of connectivity maps is performed by Schmid et al. [] predicting the Round Trip Time (RTT) in addition to the throughput. Laying their focus on the segmentation of such a connectivity map, their results showed that even for an optimal manual segmentation, the RMSRE between the measured and predicted values is at least 39.12% which leads them to conduct history based algorithms in order to predict future throughput.

II. Online Prediction Methods
The usage of Connectivity Maps is limited as the prediction has a short life-time as the mapped data is quickly outdated. Furthermore this technique as-is is only applicable to cellular communication, as V2V communication is much more short-lived and fluctuates much more as the traffic does.

Therefore most methods rely on history based throughput predictions that we may summarize as online prediction methods. As for the Connectivity Maps, the methods differ by the used and predicted data, but even more so by the schemes used, the time window of their prediction and the computational complexity.

Xu et al. [] use a machine learning framework based on regression trees in order to predict future thoughput, package loss and one-way package delay by using acquired data of the last 20 seconds. The framework is solely based on online prediction and required no offline training, making it easily deployable, but possibly less optimized for different situations. Tests were conducted in various 3G networks, but without explicit tests for moving nodes, for which a prediction is more difficult compared to (nearly) stationary nodes, but which can possibly provide additional data for prediction using their environmental sensors.

RELATED WORKS?
Traditional history based prediction schemes can be classified into the three methods: Sum-of-Sinusoids (SOS) Model, Basis Expansion (BE) Model and Autoregression (AR) Model.
Common to these traditional methods is their time frame, predicting only several milliseconds into the future for high velocity nodes. This time frame is small, but enables adaptive transmission techniques such as adaptive modulation, channel coding or power control and even adjustments in high level applications in contrast to using estimated CSI, which is instantaneously outdated at higher velocities.
The aforementioned AR model uses the outdated CSI in order to predict the future CSI, meaning that no knowledge of physical parameters is needed.

Early research using this technique was conducted by Duel-Hallen [][], in which MMSE estimates of the future CSI are computed by tracing the changes in the communication channel based on outdated CSI. The other two traditional techniques are being compared, but could not hold up in terms of prediction range and computational complexity in statistical channel models or measured data.
Another study in this area of research was conducted by Zeng et al. Trying to achieve larger prediction windows compared. As the prediction of CSI is very short-lived in V2X scenarios as of the changing channel conditions, they use an autoregressive model to
The authors identify the difficulty of predicting the performance in V2X scenarios using CSI as the CSI is not always accurate and outdated quickly caused by the fast changing channel conditions. Their solutions is a channel prediction and scheduling scheme using RSUs and Control Servers which receive data for prediction of the best relay of the connected vehicles. The prediction is achieved using current velocity, position and decoding status of each vehicle in an autoregressive model resulting in a value for the large scale fading. Using that value, a centralized scheduling scheme is applied, which according to the authors reduces the overhead as the vehicles only report the most basic information on each dissemination cycle and therefore yield a faster data transfer as shown in different simulation scenarios.

METHODS
Important steps in prediction: algorithm → gather, extract, predict, adjust, feedback
other studies imply also the dissemination of these prediction, interesting rather in V2V platooning scenarios

In order to maintain a structure in the vast amount of partially very similar works, this study tries to categorize the
Kelch et al

In order to maintain the oversight over the vast amounts of works, from which many are similar to the core, this work tries to first elevate a structure to which we adhere throughout the rest of the study.
Important elements for a prediction of the network quality are the estimation/measurement, the prediction and the dissemination of relevant data.
These terms need to be explained further:
- Estimation/Measurement refers to the calculation of current network indicators. These can vary from channel parameters such as RSSI, CQI, used cells etc. to connection specific measurements such as latency, RTT, throughput and so on
- Prediction is the art of using estimated or measured indicators in order to make a statement about the future connectivity in terms of defined indicators
- Dissemination
The works can be categorized by different sets of features, such as the network technology to which they can be applied, the algorithms used or the indicators predicted.
Judging by the majority of works, they can be grouped into two different sets in terms of their predictions methods: The online prediction using measurements from the recent past and appropriate algorithms such as machine learning while the offline prediction relies on previous measurements mapped to a certain location.